## Slide 1: Binary Representations
Presented By:
Elizer Ponio Jr. Department of Computer Science
College of Computing and Information Technologies

## Slide 2: Binary Representations
There are several representations used to represent a decimal number to a binary number.
Signed magnitude representation
One’s complement representation
Two’s complement representation

## Slide 3: Signed Magnitude
A representation in which we express a decimal number as a positive or negative binary number using its most significant bit.
It uses the Most Significant Bit (MSB) as the sign bit.
The MSB is the leftmost bit in a binary number.
For example,
1
0
1
1
0
1
1 is the most significant bit

## Slide 4: Signed Magnitude
In Signed Magnitude Representation, the sign of the number is interpreted as follows:
0 means Positive
1 means Negative
The magnitude is the size of the number irrespective of sign.
For example, the numbers +13 and -13 both have a magnitude of 13

## Slide 5: Signed Magnitude
Here is an example using 5-bit integer representation of +13 and -13:
Positive 13
Negative 13
01101
11101
Sign bit
Sign bit
Magnitude
Magnitude

## Slide 6: Signed Magnitude
The problem with this form of representation is that it has two representations for the number 0:
Positive 0
Negative 0
00000
10000

## Slide 7: One’s Complement
Another form of binary representation is called One's Complement.
To represent a negative number in One's Complement you simply take the numbers magnitude and flip all the bits (i.e. 1 becomes 0, and 0 becomes 1).

## Slide 8: One’s Complement
1
0
1
0
0
1
0
1
Example: Get the one’s complement of 5
1
2
4
8
Step 1: Convert 5 to binary
Step 2: Convert all 1 to 0 and all 0 to 1
Positive 5
Negative 5

## Slide 9: One’s Complement
Another example, a one’s complement representation of +13 and -13
Positive 13
Negative 13
01101
10010

## Slide 10: One’s Complement
However, this form of representation still has two representations for the number 0:
Positive 0
Negative 0
00000
11111

## Slide 11: Two’s Complement
Finally, we have the binary representation form called Two's Complement
In order to represent a negative number in Two’s complement:
Take the 1's Complement
Add 1 to the Least Significant Bit (LSB).
The LSB is the rightmost bit.
For example,
1
0
1
1
0
1
1 is the least significant bit

## Slide 12: Two’s Complement
Example: Get the two’s complement of 13
01101
Step 1: Take the one’s complement of 13
10010
1
2
4
8
16

## Slide 13: Two’s Complement
Example: Get the two’s complement of 13
Step 2: Add one to the rightmost bit
10010
1
----------
10011

## Slide 14: Two’s Complement
Example: Get the two’s complement of 12
01100
10011
1
---------
10100
-12
Step 1: Take the one’s complement
Step 2: Add one to the rightmostbit

## Slide 15: Two’s Complement
1
0
1
0
0
0 x = 0 x 1 = 0
0 x = 0 x 2 = 0
1 x = 1 x 4 = 4
0 x = 0 x 8 = 0
-1 x = -1 x 16 = -16
Answer = -12

## Slide 16: Two’s Complement Subtraction
Two’s Complement Subtraction
(+10)
(-5)
-------
5
(+10)
(+5)
-------
5
Standard Subtraction

## Slide 17: Standard Binary Subtraction
              0 0
              (-) 1 0 1
-----------
1
0
1
0
Borrow 1
1
0
Borrow 1
0
1
(+10)
(+5)
-------
5

## Slide 18: Two’s Complement Subtraction
Step 1: Take the two’s complement of the subtrahend
0 1 0 1
1 0 1 0
1
---------
1 0 1 1
1 0 1 0
0 1 0 1
---------
1 0 1 0
1 0 1 1
---------
0 1 0 1
Step 2: Perform addition